# SHUEY-JOHNS 1911 AUTO BUSHING TOOL

## USER INSTRUCTIONS

Note: This tool is designed for the Colt 1911 and clones. The tool will fit all standard bushing designs.

This tool is designed for the tightest bushing fit and will safely and positively rotate the bushing.

This tool is designed for the convenient use for both the right or left hand use. Simply remove the two screws and turn the lever plate over and replace the two screws.

Assure the 1911 Auto pistol is unloaded, with magazine removed and the chamber is clear of any live ammunition.  Please follow manufacturer’s safety procedures with original equipment manufacturer’s “OEM” manual for your 1911 auto pistol.

Follow all original manufacturers guidelines for safety and disassembly of your 1911 Auto Pistol.

# Disassemble Procedure

- Grasp firmly the unloaded pistol with the muzzle pointed up.

- With the other hand place the tool over the bushing (as shown)

- Hold the tool flat against the front of the slide (as shown) to depress the spring plug down into the slide.

- Rotate the tool clockwise while the plug is forced down to clear the bushing. The plug will pop up and be captured by the tool as shown below.

- The plug is still under spring pressure! Slowly back the tool off of the slide.

- Use the pistol owner’s manual to further the pistols disassembly.

- When the tool is free of the slide and spring plug, disassemble the pistol as recommended in the owners manual.

### Reassembly procedure

- Grasp firmly the pistol in one hand with the muzzle up (just like the disassembly (as shown).

- Place the spring plug onto the spring.

- With the tool in the other hand, place the tool over the plug (as shown).

- Align the tool to fit overt the bushing and firm place the tool onto the face of the slide.

- Keeping the tool pressed firmly onto the slide, squeeze the lever plate to depress the spring and plug.

- When the plug is fully depressed and bushing is free to rotate over the plug (as shown). Rotate the tool with bushing counter clockwise until the bushing captures the plug.

- Only when No. 6 is successfully completed, remove the tool.

Note:

When this tool is use as directed the plug and spring are fully captured for safety and swift foolproof disassembly/reassembly. You will not ever have a lost or flying part. Guaranteed!

All Shuey-Johns 1911 Auto Bushing Tools come with a conditional lifetime warranty.

CAUTION:  Always wear safety glasses when using this tool. Gun springs are under pressure and can cause injury. Please fully read all directions before using this tool.